## Slide 1: MiceDCER: Algorithm Operation
Carlos Felipe Amézquita S.
Carlos Felipe Estrada Solano
Oscar Mauricio Caicedo Rendón
Nelson Luis Saldanha da Fonseca

## Slide 2: Introduction
Software-Defined Networking (SDN):
  Innovative paradigm in network design and management.
  Separates the control plane from the data forwarding plane.
  Tackles the limitations of traditional networking architectures.
SDN is used for routing different flows in Data Center Networks (DCN).

## Slide 3: Introduction
The problem of actual routing proposals is the delay introduced in the mice flows.
  Mostly caused by the number of routing rules installed in the switches by the SDN controller (scalability problem).
  Using static rules by ECMP results in a high number of source-destination rules.
  Installing rules dynamically for each incoming flow can also result in an overload in the controller.

## Slide 4: Introduction
MiceDCER (Mice Data Center Efficient Routing)
  A network algorithm that handles the installation of rules.
  Enables an efficient routing, regarding the delay, of mice flows in SDN-based DCNs.
  Relies on the ARP messages and the addresses of edge switches.
  The objective of MiceDCER is to reduce the number of rules installed on the switches.

## Slide 5: Process
Initialization
Generating Pseudo-MACs (PMACs)
Storing PMACs in tables
Intercepting Message
Message Processing
Checking Port and IP
Replying Message
Routing Process

## Slide 6: Initialization
Deploy Network Topology
  Connection between switches only (without host connection)
Pre-configuration
  OpenFlow switches can work in any layer (either Layer 2 or Layer 3)
  The defined ID (DPID) determines the level of the switches to be connected (core, aggregate or edge).

## Slide 7: Initialization
The switch DPID is a 64-bit value:
  The 48 least significant bits (LSB) correspond to the switch MAC.
  The 16 most significant bits (MSB) depend of the implementation of the switch.
  This implementation varies with each model:
    HP Comware: OpenFlow instance ID
    Mellanox: Any value

## Slide 8: Initialization
For example (see below):
  HP Comware: 002839C3205B9FA4
  Mellanox : XXXX39C3205B9FA4 (XXXX can be any value)
The MSB of the DPID determine the level of the switch within the topology.
Switch | 
MAC | 39:C3:20:5B:9F:A4
OF Instance | 40

## Slide 9: Initialization
When connecting the switches to the logically centralized controller:
  Install initial rules:
    (1) ARP -> Controller
    (2) ARP -> FLOOD
  Perform Topology Discovery to check the switches connected and their connections.
  Topology Discovery is continually running in the controller, and completes when there are no longer changes in the network topology.

## Slide 10
Core
Aggregate
Edge / ToR
  (1) ARP -> Controller
  (2) ARP -> FLOOD
(I)
(I)
(I)
(I)
(2)
(2)
(2)
(2)
(2)
(2)

## Slide 11: Initialization
Pseudo-MACs (PMACs):
  Internal addresses that determine the location of the hosts in the topology.
  End hosts themselves maintain their actual MACs (AMACs).
  Each part of the PMAC reflects the hierarchical location of the host.
  PortLand uses PMACs for efficient forwarding, routing and VM migration.

## Slide 12: Initialization
MiceDCER assigns PMACs for the edge switches and the hosts.
The PMAC generated depends of the position of the topology.
There are four components: pod, position, port, and virtual machine ID.

## Slide 13: Initialization
MiceDCER checks how the edges are connected:
  After Topology Discovery completes, but before hosts start communicating.
  It is assumed that the first edge switch contains the initial pod and position numbers.
  The number of hops between edge switches determines if the edge is in the same pod or in a different pod.

## Slide 14
Pod 1, pos. 1
  The number of hops determines the pod where the switch belongs.
Pod 1, pos. 2
Pod 2, pos. 1
Core
Aggregate
Edge / ToR
(I)
(I)
(I)
(I)
(2)
(2)
(2)
(2)
(2)
(2)
2 hops: Same pod
4 hops: Different pod

## Slide 15: Initialization
MiceDCER stores the pod and position values of the switches in a table:
  The table has an identifier which can be either the switch MAC or the DPID (which contains the MAC).
  It provides two fields for the pod and position assigned.
MAC | Pod | Position
EC:DA:39:88:92:0E | 1 | 1
AA:3A:58:9F:B8:FD | 1 | 2
41:E1:FB:E5:D0:5B | 2 | 1
71:78:87:DD:E4:E7 | 2 | 2

## Slide 16: Initialization
Initialization process:
  When a switch connects, it will be added to a group corresponding to its level.
  It will also install the ARP rule for the switch (to the controller or FLOOD).
  If it is an edge switch, an entry with its pod and position numbers is created on the table (depending of existing entries).

## Slide 17: Generating Pseudo-MACs (PMACs)
When a host connects to the switch, the controller assigns the PMAC:
  The pod and position are taken from the switch connected.
  The port indicates the port number that connects the switch to the host.
  The virtual machine ID corresponds to the nth system of the host connected to the same port.

## Slide 18: Generating Pseudo-MACs (PMACs)
Core
Aggregate
Edge / ToR
1
2
Position
1
2
1
2
1
2
1
2
1
2
1
2
Port
Pod
The dotted links indicate that the hosts have not yet initiated the communication.

## Slide 19: Generating Pseudo-MACs (PMACs)
Virtual Machine ID
1
2
3
4

## Slide 20: Generating Pseudo-MACs (PMACs)
MAC | Pod | Position | Port | VM ID | PMAC
03:45:21:A2:4B:61 | 1 | 1 | 1 | 1 | 00:01:00:01:01:01
 |  |  |  | 2 | 00:01:00:01:01:02
 |  |  |  | 3 | 00:01:00:01:01:03
4C:D9:E0:3E:2C:8F | 1 | 1 | 2 | 1 | 00:01:00:01:02:01
1C:5F:76:6D:14:E1 | 1 | 2 | 1 | 1 | 00:01:00:02:01:01
 |  |  |  | 2 | 00:01:00:02:01:02
B5:8F:78:59:FA:2E | 1 | 2 | 2 | 1 | 00:01:00:02:02:01
61:CF:28:2F:26:83 | 2 | 1 | 1 | 1 | 00:02:00:01:01:01
 |  |  |  | 2 | 00:02:00:01:01:02
56:64:8A:FA:94:69 | 2 | 1 | 2 | 1 | 00:02:00:01:02:01

## Slide 21: Storing PMACs in tables
MiceDCER provides a table (or array) for storing PMACs for the end hosts.
This table stores the PMAC according to the actual host MAC (or the DPID) and the virtual machine IP address.
The PMAC is stored as a MAC-formatted string.

## Slide 22: Storing PMACs in tables
MAC | IP | VMID | PMAC
03:45:21:A2:4B:61 | 150.0.11.1 | 1 | 00:01:00:01:01:01
 | 150.0.11.2 | 2 | 00:01:00:01:01:02
 | 150.0.11.3 | 3 | 00:01:00:01:01:03
Edge / ToR

## Slide 23: Storing PMACs in tables
PMAC generation and storage process:
  The pod and position are taken from the entry in the pod-position table corresponding to the switch ID.
  The port is the number of port to which the host is connected to the switch.
  The virtual machine ID comes from the index of a list of VM IP addresses corresponding to the host MAC.

## Slide 24: Installing Rules on PMAC assignation
The controller installs the rules as the PMACs of the hosts are assigned.
As shown before, the MSB part of the DPID determines the level of the switch.
Therefore, the controller installs the rules according to the level of the switches.

## Slide 25: Installing Rules on PMAC assignation
The route through a core or an aggregate is determined by PMAC wildcards.
  Core example: 00:3B:*:*:*:* (for any PMAC with pod 00:3B)
A single route is installed in the edge if the two hosts communicating are connected to the same switch.

## Slide 26: Installing Rules on PMAC assignation
The rules of the core switches are only dependent of the destination pod.
The rules of the aggregates are set as follows:
  For each port connecting to an edge switch, a rule (high priority) containing the aggregate pod and edge position is installed.
  A global rule (low priority) is installed for the ports connecting to the core switches.
  Group type action is used for sending through the ports.
Notes: The aggregate pod number is obtained from the nearest edge checked.

## Slide 27: Installing Rules on PMAC assignation
The rules for the edges are the following:
  For each port connecting to a host, a rule (high priority) containing the pod and position of the edge, and the number of the port connecting to that host is installed.
  To highlight, the PMAC-AMAC conversion is done at the edge switch, so the rules to the hosts will use AMACs.
  A global PMAC rule (low priority) is installed for the ports connecting to the aggregate switches.

## Slide 28: Intercepting Messages
When hosts start communicating, they do not know the MAC of the host which has the destination IP.
The source host sends a flow containing an ARP message to the edge switch.
The switch sends the arriving ARP message to the controller.
Controller
(I)
(3)
Edge / ToR
10.0.0.1
10.0.0.2
SEND

## Slide 29: Message Processing
The controller processes the inbound data contained in the message.
Layer 2
Layer 1
ARP | 
Operation Code | 1
Source MAC | 03:45:21:A2:4B:61
Source IP | 10.0.0.1
Destination MAC | 00:00:00:00:00:00
Destination IP | 10.0.0.8
Port | 1
ARP

## Slide 30: Message Processing
The Operation Code determines if the message is a request (1) or a reply (2).
In this case, the message is a request for the MAC corresponding to the destination IP address.
Layer 2
Layer 1
ARP | 
Operation Code | 1
Source MAC | 03:45:21:A2:4B:61
Source IP | 10.0.0.1
Destination MAC | 00:00:00:00:00:00
Destination IP | 10.0.0.8
Port | 1

## Slide 31: Message Processing
Source Host
Destination Host
The switch needs to know the MAC belonging to this host.
Core
Aggregate
Edge / ToR
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
10.0.0.5
10.0.0.6
10.0.0.7
10.0.0.8

## Slide 32: Checking Port and IP
The routing process of the ARP message is done following the ARP rules.
According to this, when the ARP message arrives to the edge switch, it is sent to the controller.

## Slide 33: Checking Port and IP
The controller checks the destination IP address of the message sent by the switch.
If the IP is known by the controller, a reply ARP message is sent back to the source host.
If the IP is not known, the controller indicates the receiving switch to FLOOD.
Controller
Edge / ToR
10.0.0.1 UNKNOWN
FLOOD

## Slide 34: Checking Port and IP
The generated messages are sent to the rest of switches and hosts:
  Hosts that do not match the IP destination address will reject the message.
  When the switch is a core or an aggregate, it is indicated to FLOOD.
  When the switch is an edge, it sends the message to the controller and the process repeats.

## Slide 35: Replying Message
The destination sends back a reply when receiving the ARP request.
This reply message contains the PMAC of the request destination host.
Since the controller now knows the IP of both hosts, the reply is sent to the source host as normal.

## Slide 36: Replying Message
Core
Aggregate
Edge / ToR
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
10.0.0.5
10.0.0.6
10.0.0.7
10.0.0.8
* FLOOD messages are not shown
Request
Reply

## Slide 37: Routing Process
Once the MAC corresponding to the IP address of the communicating host is known, the routing process can start.
  If a packet is routed to another host that is connected to the same edge, it is simply sent to the port connected to that host.
  Otherwise, it is routed to the ports connecting to the upper switches, using the PMAC-AMAC conversion.
  There are several paths that can be taken between switches.

## Slide 38: Routing Process
Core
Aggregate
Edge / ToR
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
10.0.0.5
10.0.0.6
10.0.0.7
10.0.0.8

## Slide 39: Work In Progress
Perform tests on a real OpenFlow switch: How the number of rules affect delay?
Develop the algorithm for SDN application framework (e.g. Ryu).
An analytic and experimental evaluation.